## Slide 1: TACACS+ RFC Proposal
Presenters: Thorsten Dahm (Google), Andrej Ota (Goolge), Douglas Gash (Cisco)

## Slide 2: Agenda
TACACS+ Background
Proposed Transport Security
Proposed Deprecations
Open Questions

## Slide 3: TACACS+ Background
Current Informal standard defined by TACACS+ Draft 1998
  Standards Process Never completed.
Widespread adoption for Device Administration Role:
  Mediate the access of devices for configuration update.
  Network Access Role delegated to RADIUS
Why Seek standardization Now?
  Ambiguity Resolve and Tidy up.
  Enhance Encryption

## Slide 4: Proposed Transport Security
Current Encryption (MD5) is not regarded as secure
Require Full backwards compatibility.
Propose to add Transport Security
  Options:
    Separate Port
    Start TLS (Preferred/Documented option)

## Slide 5: Crypto Proposal Detail
Modeled on established StartTLS based protocols
Add new TACACS+ packet Type 0: StartTLS
  Client sends as first packet in connection
  Content of first packet is ClientHello
  If Server accepts then responds with ServerHello,
  Handshake then proceeds to upgrade connection.

## Slide 6: Proposed Deprecations
Remove SENDPASS option (Previously marked deprecated)
Removed Normative parts of Legacy Elements of protocol:
  ARAP
  SendAuth

## Slide 7: Open Questions
Confirm StartTLS approach vs Separate TLS port
  Proposal: StartTLS
Identify whether Authorization and Accounting attributes should be regulated.
  Proposal: Not to regulate due to overhead.
  Namespacing (such as Vendor number in RADIUS VSA) would break backwards compatibility

## Slide 8: Q&A